## Slide 1: Trends in Iberoamerica’s Mobility
XXV General Meeting
Latin America Metro and Subway Association
Guadalajara, Jalisco
22 November 2011
Integral Mobility Systems
for Metropolis
Dr Vukan R Vuchic
Emeritus Professor
University of Pennsylvania

## Slide 2: Presentation Outline
Present Condition of Urban Transportation
Development of Transportation and Cities in the 20th/21st Centuries
The Family of Urban Transportation Modes Today
Rational Transportation Policy Formulation Requirements
Intermodal Policies and Implementation Measures
Rail and Intermodal Transit Systems
Rail Transit Lines and Networks Planning and Design
Special Lines and Operations
Stations: Types, Locations and Spacings
Review of Experiences and Prospects in Urban Transportation

## Slide 3
Present Condition of Urban Transportation,
Progress and Problems
Present transportation systems provide:
  Very high mobility for population
  Great economic and lifestyle benefits
Problems remain:
  Quality of service, speed and reliability are often unsatisfactory
  Inequities and serious problems of auto dependency and neglected other modes: public transit, walking, bicycling
  Transportation produces negative impacts on cities and their livability or quality of life

## Slide 4
Development of Transportation and Cities
in the 20th/21st Centuries
- The twentieth century started with rapid growth of cities and industrialization
- Around 1900, mechanical transportation was just introduced
- Initially “Walking Cities” were upgraded by the invention of electric transit (public transportation)
- Between 1900 and 1950 development of “Transit Cities:”
  Extensive transit services on streets
  Independent, high-performance systems - metro or rapid transit

## Slide 5
Development of Transportation and Cities
in the 20th/21st Centuries (cont.)
- In the USA from 1930, and other countries from 1950:
  Creation of “Automobile Cities”
  Maximum growth of highways during the 1950-70 period
- The field of Traffic Engineering was developed
- Cities which focused on automobile-truck and highways while neglecting transit and pedestrians created major problems:
  Congestion
  Excessive highway and parking construction
  Non-auto users have become second-class citizens
- Today, cities with largest motorway/Autobahn systems have most severe congestion, deteriorated environment and quality of life.

## Slide 13
Development of Transportation and Cities
in the 20th/21st Centuries (cont.)
- Studies of urban transportation policies suggest:
  Relationship of cities and transportation is very complex
  “Systems Approach” is necessary
  There is a need to recognize quality of life or “livability”
- Since the 1970’s focus has been on developing “Intermodal Cities:”
  Large cities relying on a number of coordinated modes
  More travel choices
  Improved efficiency, comfort, safety and reliability
  Reduce negative environmental impacts
  Refocus on human scale activities

## Slide 14
The Family of Urban Transportation Modes Today
Intermodal cities rely on many modes of transport - each one has its strengths and limitations. The family of modes includes:
  Street / road system with automobiles, trucks, bicycles
  Basic network in every city
  Two major social benefits: convenience and ubiquity
  Traffic engineering and ITS becoming more important
  Walking
  Optimal mode for high density travel
  Environmentally friendly
  Key component of urban “livability”

## Slide 15
The Family of Urban Transportation Modes Today (cont.)
  Bus transit
  Lowest cost mode of public transportation
  Does not compete easily with private auto
  Upgrading to Bus Rapid Transit intensified
  Tramway and Light Rail Transit:
  Many innovations in recent decades
  Filling the gap: higher performance than bus, less expensive than metro
  Built in medium and large cities (15 new systems in North America, many in Europe)
  Many diverse applications

## Slide 16
The Family of Urban Transportation Modes Today (cont.)
  Metro or Rail Rapid Transit
  Highest capacity – lowest land and energy consumption
  Very effective in large urban areas
  Speed and reliability make it competitive with private car
  Regional Rail
  Taxi, minibuses, jitneys
  Automated Guided Transit (AGT)
  Intermodal Transit System:
  Operationally and organizationally integrated modes

## Slide 23
Photo 5.24 TransMilenio BRT
Courtesy: TransMilenio BRT, Bogota, Columbia

## Slide 25
Photo 5.29 Boston Silver Line

## Slide 51: 4.1 Rational Transportation Policy Formulation Requirements
Understanding transport
function and interactions
Define goals and objectives
Future travel
Design transport system
and facilities
Build and operate
transport system
Conditions and trends
Technical expertise
Organization and
management
Political and
public support
Financing

## Slide 52: 4.2 Functional Role of Transport in a City
City
Economy
Government
Industry
Environment
Housing
Social conditions
Culture and
recreation
Transport

## Slide 53
4.5 Conceptual Structure of Urban Transportation Planning
LEVEL IV
Planning, design, operation of single facility
LEVEL III
Coordination of single mode network/system
LEVEL II
Integration of multimodal network/system
LEVEL I
City – transport balance
Plaza
Intersection
Single route
Urban streets
Transit network
Transit
Auto-highway
Pedestrian
Economy
Housing
Social conditions
Environment
Transport
CITY
or

## Slide 54
I. DEFINE TYPE OF CITY/SOCIETY
II. DETERMINE MODE COMPOSITION
III. DESIGN MODE NETWORKS
IV. DESIGN INDIVIDUAL FACILITIES
4.6 Planning Level Sequence in Urban Transport:
Hierarchy of goals and objectives

## Slide 55
5. 1 Intermodal Policies and Implementation Measures
Having understood the fundamental problems, transportation professionals should balance
Individual Behavior and System Optimum by:
Transit incentives: building high-quality, competitive transit systems, fare innovations, positive attitude toward passengers, marketing, etc.
    Transit incentives are easily justified and popular
    Auto disincentives: traffic reduction policies, economic policies (parking rates and structure, road pricing)
    Politically more challenging, but justified and rational.

## Slide 56
0
2
4
6
8
10
Cost [$/person-trip]
Bus / LRT / Metro
Auto
Large City - Peak
5.2 Implementation Policies and
Implementation measures (cont.)
Auto Peak
without
Parking, Tolls
Express Bus /
Regional Rail
Toll
Parking
Gasoline
Fare
Direct costs of urban travel by different modes

## Slide 57
20
15
10
5
0
5
10
Cost [$/person-trip]
5.3 Implementation Policies and
Implementation measures (cont.)
Bus / LRT / Metro
Auto
Large City - Peak
Auto Peak
without
Parking, Tolls
Express Bus /
Regional Rail
Toll
Parking
Gasoline
Fare
Indirect
user cost
Subsidy
Environ-
mental
Social
Environ-
mental
Subsidy
Social
Total costs of urban travel by different modes

## Slide 58
    They consist of modes which are integrated in the following ways:
        Physically (joint transfer stations)
        With coordinated schedules
        Joint fares
        Integrated information.
        Rail transit is the main carrier in intermodal systems of most medium and large cities.
6.1 Intermodal Transportation Systems

## Slide 59: 6.2 Characteristics of Rail Transit
Rail transit characteristics
  Rail – simple support and guidance
  Low energy consumption
  Use of trains – very high capacity
  Separate rights-of-way: B or A
  Electric traction – no air pollution in city
High investment – high performance

## Slide 60
6.3 Three Categories of Transit Modes
by Right-of-Way Category
Category C - Street ROW, mixed traffic - Tramway
Category B – Longitudinally separated: Semirapid transit – Light Rail Transit - LRT
Category A – Full separation: Rapid transit or Metro and Regional Rail

## Slide 61: 6.4 Family of Rail Transit Modes: Definitions and Illustrations
Tramway (Streetcar)
Light Rail Transit - LRT (Light Metro)
- Light Rail Rapid Transit - LRRT
Metro/Rapid Transit (Subway, Underground, U-Bahn)
- Regional Metro
Regional Rail (Commuter Rail)
  - Tram - Train

## Slide 62
Street
transit
Rapid transit
ROW categories
C
A
Bipolarized transit: street and rapid transit
System performance: speed, reliability, capacity, image
Investment cost / line length
Bus
Metro

## Slide 63
Street
transit
Semirapid
transit
Rapid transit
ROW categories
C
B
A
Intermediate systems “filling the gap” between street transit and metros
System performance: speed, reliability, capacity, image
Investment cost / line length
Bus
BRT
LRT
Metro

## Slide 64: LINZ

## Slide 69: 7.1 Rail Transit Line and Network Planning and Design
Major elements and considerations:
Geographic layout/conditions (water, hills)
Alignments of major passenger flows
Selection of right-of-way (ROW) and transit mode
Network topology
Operating efficiency
Intermodal planning

## Slide 70: 7.2 Upgrading of Transit Modes
With increasing passenger volumes operation of many ovelapping bus lines become inefficient
Upgrading of service through consolidation of lines usually results in separation of ROW and replacement of buses by rail
Consolidation of lines is greater on rail than on bus systems, but its optimal pattern varies with many factors

## Slide 71: 7.3 Important Aspects in Transit Lines and Network Design
Geometric types and their characteristics
Alignment and ROW (tunnel depth), ROW separation
Trunks only or with branches
Independent vs integrated lines
  Trade offs
  Criteria
Compatible vs incompatible technologies
Types of stations

## Slide 72
a. Trunk with branches
b. Trunk with feeders
Radial transit lines: trunk with branches and with feeders

## Slide 73
Central
City
Buses Only
Central
City
LRT and Buses
Transfer station
Change from an extensive bus network into an intensive, more efficient and attractive LRT/Bus network (Sacramento, CA)
LRT

## Slide 74
Line Type
1 Radial with branches
2 Diametrical with branches
3 Diametrical with loop
4 Tangential (crosstown)
5 Circle or ring
6 Diametrical
Transfer station
Terminal station
Geometric forms of transit lines

## Slide 75: 7.4 Classification and Characteristics of Line and Network Types
Diametrical vs. radial lines
Types of diametrical lines: “I”, “Y”, “X”, “L”, “U”, “T”
Circle or ring lines
Single lines vs. lines with branches, how many branches?
Independent vs. integrated lines
Transit nodes: intramodal and intermodal transfers

## Slide 76: 7.5 Diametrical vs. Radial Lines
Better center city distribution
Greater line connectivity
Longer lines have higher operational efficiency
No terminals in city center

## Slide 77
Typical radial regional rail network: Metra in Chicago
Lake Michigan
McHenry
Lake
Kane
Cook
DuPage
Will
Harvard
McHenry
Fox Lake
Kenosha
Elgin
Geneva
Aurora
Joliet
Orland Park
University Park
To South Bend
93rd. St.
Antioch
Chicago CBD
Ogilvie Tr. Center
Union Station
La Salle Station
Randolph Station
Chicago CBD
G, M, H, K(Kenosha)
E, F, An
Au, O, J (North)
J (South), SB
U, 93 rd.
Line designation by terminals

## Slide 78
A radial/diametrical rapid transit network with CBD distribution Loop: Chicago
Lake Michigan
Dan Ryan
Eaglewood
Jackson Park
Douglas
Congress
Lake street
Ravenswood
O’Hare
Skokie Swift
Evanston
Midway
Downtown network
Downtown network
Purple
Yellow
Brown
Blue
Orange
Red
Red
Green
Green
Blue
“The Loop”
Br, O, P
Br, G, O, P
R
G
O
R
BL
G
G
Br
P

## Slide 79
a. Typical metro line with dominant trunk
b. Typical regional rail line with dominant branches
Diametrical lines with branches

## Slide 80: 7.6 Trunk with Branches vs with Feeders
Branches provide for passengers continuous service without transfers between center city and suburban areas
being longer lines trunk and branches have smaller percentaje of cycle times as terminal times than trunk with feeders
Transfer stations are not needed
Each feeder line can be optimized
Trunk with feeders offers more reliable service and higher performance

## Slide 81: 7.8 Independent vs. Integrated Lines
Independent lines are operationally very simple – important when capacity is reached
Integrated lines – with branches and joint sections:
+ Reduce need for transfers
+ Balancing of frequencies increases capacity utilization
+ Allow changes in line routings + Economies of single rolling stock, shops & control center

## Slide 82
A
B
F
E
C
D
Terminal Station
Transfer Station
Independent operation: 3 lines
A
B
C
D
F
E
Integrated operation: 15 routes
A theoretical transit network with independent and with integrated line operations.

## Slide 83
Cologne (Koln) LRT - a
radial-circumferential
integrated LRT network

## Slide 84
2, 4, 11, 14
14
2, 4, 11
1, 2, 4, 11
11, 14
4
2
4, 9
9, 11, 14
9, 11, 14
5, 6, 7, 15
1, 2, 4, 9, 11, 14
1, 14
5, 6, 7, 15
5, 6, 7
15
15
1, 2, 4, 11
9
1
5, 6, 7, 15
Typical light rail transit integrated network: Stuttgart center city
City hall
Main railway station
Charlotten platz
Liederhalle

## Slide 85
10
9
1
3
8
2
13
4
14
5
10
4
12
13
14
7
7b
11
3
3b
2
6
5
9
1
8
7
7b
12
13
City limits
6
11
S e i n e
S e i n e
Local
Terminal
Transfer
Stations:
The Paris Metro network: 14 independent lines.

## Slide 86
Transfer station
Terminal
Station
The Mexico Metro network: independent lines including “I”, “L” and “T” types
3
1
2
6,7
A
8
7
2
8
4,6
B
3
5
1,5,9,A
9
B
4

## Slide 88
6
2
9
3
1
6
7
1
9
2
10
7
8
4
10
5
5
5
5
Transfer station
Station
The Moscow “Metropolitan” network of independent lines – diametrical, radial and ring
8
3
4
11
11
Terminal

## Slide 89
6
2
3
1A
6
7
2
10
7
8
4
10
5
5
5
5
Transfer station
Station
The Moscow “Metropolitan” network with
possible branches for better area coverage in suburbs
8
3
4
11
11
Terminal
1B
9B
9A
9A
9B
1A
1B

## Slide 91: 7.9 Circle or Ring Lines
Advantages:
+ Serves very busy corridors – high passenger turnover
+ Provides extensive connectivity
+ Low time variations - high capacity utilization
+ Distributes and connects radials
Limitations:
- Recovery of delays is difficult
- Limited selection of service headways

## Slide 95
1,9
5
5
2
4
6
3
BRONX
QUEENS
Park/Lexington Avenue
7th Avenue
3
2
1,9
1,9
6
2
4
3
5
5
4
6
3
5
2
4
Schematic layout of the contiguous Division A network in New York City
MANHATTAN
BROOKLYN
Broadway

## Slide 97
Paris Regional Rail (RER) network: diametrical lines with 2-3 branches

## Slide 99
Miami Downtown People Mover as a feeder to Metrorail
Omni Loop
Brickel Loop
Downtown Loop
Metrorail
Omni
Downtown
Brickel
Legend:
Metrorail

## Slide 100
Light rail, rapid transit, and regional rail transit networks in Philadelphia

## Slide 101
Trunk line with branches on both sides: Philadelphia Regional Rail

## Slide 103
S5
S1, S8
S6
S1
S2
SA
S2
S7
S6
S3
S4
S5
S1
The Munich S-Bahn (regional rail) network
S3, S4, S7
S8
S27
S27
SA
Main Rwy Station
East Rwy Station

## Slide 105
San Francisco Bay Area Rapid Transit (BART) Network

## Slide 106
Schematic network of BART lines in San Francisco

## Slide 107
Three Regional Rail networks in New York:
Metro North, LIRR and New Jwersey Transit

## Slide 108
i. Separate terminals with radial lines
ii. Connected terminals with diametrical lines
a. Typical regional rail networks
i. Single transfer station
ii. Multiple transfer stations
b. Radial metro networks with different layouts
Radial rail transit networks
Possible circle line

## Slide 109: 8.1 Special Lines and Operations
Single-track lines or sections
Accelerated operations
  Skip-stop operation (2 tracks)
  Express/local operations (2, 3 or 4 tracks)
  Zonal operations
Timed Transfer Stations and Networks

## Slide 110: 9. 1 Rail Transit Stations: Types, Locations and Spacings
Classification
    In the street (tram, LRT) vs. separated/enclosed (LRT, Metro, Regional Rail)
    Intramodal transfers
    Intermodal transfers
    Terminals: permanent and temporary
Locations
Spacings

## Slide 111
  Planning and design of rail transit networks is extremely important, but knowledge about that process is rather limited
  Diametrical lines with branches are most common
  Integrated networks have many advantages over independent ones
  “Y”, “X” and “L” lines are often successfully used
  “U” lines are inferior to “I” and “L” types
  Circle lines are functionally excellent, in spite of operational problems
  Station types, locations and spacings require very careful planning, mistakes are very costly
  Special lines (skip-stop, express, zonal and single track) can be very effective for speeding up services and increasing efficiency
9.2 Case Studies of Rail Transit Networks:
Successes and Problems

## Slide 122: 10.1 Review of Experiences and Prospects in Urban Transportation Examples of Conditions in Several City Categories
A. Developing countries
Many cities in Africa, Latin America and Asia face most of the listed problems:
Understanding of transportation and its role in city is often insufficient
Program of financing, particularly investments, is unstable and inadequate because of other country’s needs
Lack of financing favors low-investment/low-quality transport systems
Limited technical and managerial expertise

## Slide 123: 10.2 Examples of Several City Categories
B. Countries in transition: East European countries, Russia, former Soviet republics, China
- Excellent technical expertise for transit systems, but lagging in highway/traffic engineering
- Inadequate understanding of intermodal complexities and rapid increase of auto ownership lead to repetition of many errors industrial countries made at the corresponding stage of transport development
- Missing systems approach leads to inefficiencies
- Failure to develop medium-capacity transit modes – LRT and BRT

## Slide 124: 10.3 Examples of Several City Categories
C. Many cities in industrialized countries
Limited understanding of complex urban transport problems
Land use-transportation planning seldom coordinated
Insufficient intermodal integration
False claims that in large cities traffic congestion is inevitable is still widespread
- Special interests confuse situation by proposing paratransit, monorails and personal rapid transit as “optimal solutions”

## Slide 125: 10.4 Examples of Successful Cities and Their Lessons
D. Industrialized Cities Leading in Transportation Solutions
Several European, North American and Asian cities have solved most barriers and developed rational transportation systems:
- Munich, Oslo, Zurich, Stockholm, Vienna, Copenhagen, Stuttgart
- Portland, San Francisco, Toronto, Vancouver
- Singapore, Hong Kong

## Slide 136: 10.5 Review of Measures in Leading Cities
The leading cities show that they have solved most barriers to rational transportation, such as:
      Excellent Metro systems
      LRT systems integrated in many pedestrian-oriented cities in Germany, France, Spain and United States
      Well organized bus and BRT services
      One “umbrella” authority coordinates all transport modes

## Slide 137
  Area Licensing Scheme, upgraded into Electronic Road Pricing – ERP prevents traffic congestion; introduced in Singapore in 1975, later in several North European cities
  Extensive intermodal coordination is implemented in German, Swiss, Scandinavian and North American cities
  Consistent improvements of transit systems, intermodal integration, human orientation for livable cities
  Pedestrians are a protected and promoted mode of travel
  Public policies integrate elements of city livability and sustainability.

## Slide 138: 10.6 Rational Transport Policy Formulation and Implementation
Understanding transport
function and interactions
Define goals and objectives
Future travel
Design transport system
and facilities
Build and operate
transport system
Conditions and trends
Technical expertise
Organization and
management
Political and
public support
Financing

## Slide 139: 10.7 Conclusions: Lessons for the Future
As a vital service in cities, transportation must be coordinated with other functions, such as economy, social conditions and quality of life
The goal in transportation planning should be not only efficient transportation, but creation of livable cities with good quality of life.
Well informed public generally supports balanced policies toward intermodal transportation system and livable cities
While technological innovations continue to be important, understanding of problems and introducing innovative policies are usually the basic initial steps toward solutions.